# Amp 2
This will be a AB763 Deluxe Reveb clone with the dry input channel replaced with a paralle triode input. The normal FMV tone circuit will be replaced by a Baxandal style passive tone circuit. Then recovery tube will be either a normal 12AX7 bypassed cathode amplifier circuit or another parallel triode stage. This input and the original wet input will be connected to the reverb and tremolo if possible using the robrob mod.
## TODO
### Circuit Design
Parallel triode input
Baxandal
Recovery: parallel as well?
Coupling two inputs to reverb/trem
Review ab763 for compatibility
Power supply

### Layout
Controls
Input stages on turret board
trem
Power supply on same turret board
Reverb unit
Tubes
On switch / cables / fuses
Speaker / chassis
Cabinet / speaker

### Parts
Cabinet
Speaker
Output Transformers
Tubes
Passives
Turret board stuff
Turret tool - build at work
### Names and Knobs

Mini-Fridge
Poet

Earthtone? Depends on color
Lux

Knobs

(normal) Volume	Treble	Middle	Bass	(wet) Volume	Treble	Bass	Reverb	speed	Intensity
Language	Brevity	Formality	Verbosity	Color	Contrast	Saturation?	Space	Time	Gravity
				Flavor

Link

Parallel 12ax7 gain stage
https://www.ampbooks.com/mobile/amp-technology/parallel/